## Slide 1
IP Networks

## Slide 2: “Hourglass design” of the internet
Source: https://oer.gitlab.io/DS/DS02-Internet.html#/slide-internet-architecture
Internet Architecture with narrow waist
IP is focal point
“Narrow waist”
Application independent!
Everything over IP
Network independent!
IP over everything

## Slide 3: IP Addresses on a network

## Slide 4
We want to communicate from one computer to another.

## Slide 5
We want to communicate from one computer to another.
So we connect them to a network. Each computer can send data to the network and see data from other computers on the network.

## Slide 6
100
2
15
1
We want to communicate from one computer to another.
So we connect them to a network. Each computer can send data to the network and see data from other computers on the network.
The computers are each given a number. The number is used to see, who sends data and who should receive it.

## Slide 7
100
2
15
1
From: 100
To: 15
Data: hello

## Slide 8
100
2
15
1
From: 100
To: 15
Data: hello
From: 100
To: 15
Data: hello
From: 100
To: 15
Data: hello

## Slide 9
100
2
15
1
From: 100
To: 15
Data: hello
From: 100
To: 15
Data: hello
From: 100
To: 15
Data: hello
Not for me.
Ignore!
Not for me.
Ignore!
For me 
Accept data.

## Slide 10: IPv4 addresses
192.168.1.100
192.168.1.2
192.168.1.15
192.168.1.1
IPv4 addresses are 32 bits long. They are written as 4 bytes.
E.g. 192.168.1.100

## Slide 11: IP Address format
https://cidr.xyz/
Networks can be split in to subnets. A subnet has an IP address range, which are the addresses usable in that network.
Data is routed inside a subnet.
The 32 bit IP addresses used in the subnet is split in NETWORK and HOST parts.
The 32 bits set to 1 in the NETMASK specifies the NETWORK part. The bits set to 0 defines the HOST parts.
The NETWORK part of an address can also be specified in CIDR format (Classless Inter-Domain Routing).
The IP address ending with .0 or .255 can not be used by a HOST.

## Slide 12: Local IP Networks
Portions of the IPv4 space are reserved for specific uses.
Loopback
  127.0.0.0 to 127.255.255.255
  Typically 127.0.0.1 is “loopback” or “localhost”
Private networks
  10.0.0.0 to 10.255.255.255
  172.16.0.0 to 172.31.255.255
  192.168.0.0 to 192.168.255.255
Any computer that is not hooked up to the internet directly (any computer that goes through a router or other NAT system) can use these addresses at will.
Source: https://www.digitalocean.com/community/tutorials/understanding-ip-addresses-subnets-and-cidr-notation-for-networking
Notes: There are also some portions of the IPv4 space that are reserved for specific uses.
One of the most useful reserved ranges is the loopback range specified by addresses from 127.0.0.0 to 127.255.255.255. This range is used by each host to test networking to itself. Typically, this is expressed by the first address in this range: 127.0.0.1.
Each of the normal classes also have a range within them that is used to designate private network addresses. For instance, for class A addresses, the addresses from 10.0.0.0 to 10.255.255.255 are reserved for private network assignment. For class B, this range is 172.16.0.0 to 172.31.255.255. For class C, the range of 192.168.0.0 to 192.168.255.255 is reserved for private usage.
Any computer that is not hooked up to the internet directly (any computer that goes through a router or other NAT system) can use these addresses at will.

## Slide 13: Public address vs. Local network address
Michael’s network.
192.168.99.0/24 is local addresses. They are managed by Michael.
5.186.34.131 is the public address. It is managed by Fibia (the internet provider).

## Slide 14: Exercise
Exercise:
  Find your LAN IP address and exchange address with another student.
  What subnet are you on?
  Ping each others machines
    Ping is probably blocked in your windows firewall.
    Try to ping 8.8.8.8 (google DNS) or Michaels Raspberry Pi if he remembered to bring it.
  Find your external (WAN) IP Address using https://www.whatsmyip.org/ or https://ifconfig.me
Linux / Mac: Windows:
Notes: https://www.thewindowsclub.com/how-to-allow-pings-icmp-echo-requests-through-windows-firewall

## Slide 15: Ports
A machine has an IP address and 65535 Ports.
A program on a machine can listen to a specific port.
A program on another machine will specify the IP address and port it wants to communicate with.

## Slide 16: Reserved ports
Ports from 0 to 1023 are reserved.
Examples:
  20 FTP — Data
  21 FTP — Control
  22 SSH Remote Login Protocol
  23 Telnet
  25 Simple Mail Transfer Protocol (SMTP)
  37 Time
  53 Domain Name System (DNS)
  80 HTTP
  110 POP3
  119 Newsgroup (NNTP)
  443 HTTPS
  546 DHCP Client
  547 DHCP Server
Wikipedia has a complete list of reserved ports:
https://en.wikipedia.org/wiki/List_of_TCP_and_UDP_port_numbers

## Slide 17: TCP / IP
Transmission Control Protocol (TCP) is a transport protocol that is used on top of IP to ensure reliable transmission of packets.
It handles retransmission of lost packages, reception of out-of-order packages and congestion control.

## Slide 18: UDP / IP
User Datagram Protocol (UDP) is a lightweight data transport protocol that works on top of IP.
Detects and discards corrupt packages. Does not handle lost or out of order packages.
It's often used for time-sensitive applications (such as real-time video streaming) where speed is more important than accuracy.

## Slide 19
Address assignment
  DHCP
  MAC address
Naming
  DNS lookup

## Slide 20: Example router setup

## Slide 29: References and image sources
https://www.digitalocean.com/community/tutorials/understanding-ip-addresses-subnets-and-cidr-notation-for-networking
https://fab.cba.mit.edu/classes/961.04/people/neil/ip.pdf
https://iximiuz.com/en/posts/computer-networking-101/
https://www.youtube.com/watch?v=PwWhJEJVGl4
https://www.youtube.com/watch?v=NyZWSvSj8ek
https://www.youtube.com/playlist?list=PL7zRJGi6nMRzg0LdsR7F3olyLGoBcIvvg